## Slide 1: A General Purpose, Open-Source Overset Library for Caelus based on Suggar++
Dr. Chris Sideroff
Dr. Darrin Stephens

## Slide 2: Overset with OpenFOAM
Previous library/solver efforts:
  foamedOver (Boger et al, PSU-ARL)
  naoeFOAM-os-SJTU (Shen at al, Shanghai Jiao Tong University)
  Others?
Previous OGA efforts:
  OperaFOAM (Chandar et al IHPC Singapore)
  Bellerophon (Groß, Univ. of Rostock)
  Others?
None have been publicly released or available for purchase (to our knowledge)

## Slide 3: Library
Caelus (OpenFOAM derivative) is collection of libraries
Goals:
  Hide overset-specific details
  Minimal changes to existing library and top-level applications
  Use existing linear solvers
  Minimal changes to existing workflow
  Use Suggar++ for OGA
Features
  Static, prescribed and dynamic motions
  6-DoF ODE solver w/ constraints, restraints and loads
  No restriction on parallel decomposition
  static/dynamic, single-phase/VOF solvers

## Slide 4: Implementation
oversetFvMesh: derived from fvMesh class
Important because (almost) all existing top-level functionality uses fvMesh
  Inherits all non-overset functionality
  Handle overset specific duties with virtual and overloaded functions
class oversetFvMesh : public fvMesh
{
…
}

## Slide 5: Low Level Changes
Few changes required to main Caelus library to support oversetFvMesh library. E.g.
  Dummy equation and matrix manipulation functions for non-overset
  Small matrix support for 6 DoF ODE functionality
  Find functions for mesh primitives required virtualization
primitiveMesh
polyMesh
fvMesh
oversetFvMesh

## Slide 6: Implementation
Manipulate matrix and field values of fringe cells
Templated matrix (momentum, pressure) and field (volume fraction) update functions
Calls DiRTlib and libSuggar++ to update fringe
fvVectorMatrix Ueqn
(
fvm::ddt(U) +
fvm::div(phi, U) –
fvm::laplacian(nu, U)
==
- fvc::grad(p)
);

## Slide 7: Implementation
Manipulate matrix and field values of fringe cells
Templated matrix (momentum, pressure) and field (volume fraction) update functions
Calls DiRTlib and libSuggar++ to update fringe
// Update matrix implicitly
mesh.updateFvMatrix<vector>(UEqn);
UEqn.solve();
// Update matrix implicitly
mesh.updateFvMatrix<vector>(UEqn);
// Update field value explicitly
mesh.updateFvField<scalar>(alpha1);

## Slide 8: Usual Workflow
Generate Mesh
Setup Case (BCs, etc)
Solve Eqns
Post Process
Assemble Matrix
Solve Matrix

## Slide 9: Overset Workflow
Generate Mesh
Setup Case (BCs, etc)
Solve Eqns
Post Process
Assemble Matrix
Solve Matrix
Run Suggar++
DCI /
libSuggar++
Modify Matrix

## Slide 10: Case Structure
├── 0
│ ├── U
│ ├── p
│ ├── k
│ ├── omega
│ └── nut
├── 1
│ ├── U
│ ├── ...
│ ├── polyMesh
│ └── uniform
│ │ └── sixDoFRigidBodyState
├── constant
│ └── polyMesh
├── suggar
│ ├── DCI
│ ├── Grids
│ │ ├── background
│ │ └── sphere
│ ├── Input
│ └── Work
└── system
├── controlDict
├── fvSchemes
└── fvSolution
FoamFile
{
version 2.0;
format ascii;
class dictionary;
location "0/uniform";
object sixDoFRigidBodyState;
}
centreOfRotation ( 4.099396 0 1.650153 );
principalOrientation ( 1 0 0 0 1 0 0 0 1 );
velocity ( 1.0e+01 0.0 0.0 );
acceleration ( 0.0 0.0 0.0 );
angularMomentum ( 0.0 0.0 0.0 );
torque ( 0.0 0.0 0.0 );

## Slide 11: Features
Suggar++ for OGA:
  DCI files (DiRTlib)
  DCI files or in memory (libSuggar++)
Static (DiRTlib)
Prescribed
  Single body, rotation or translation (DiRTlib)
  Multi body, more complex prescribed motions (libSuggar++)
Dynamic
  Multi body
  Hierarchical body arrangement (mimics Suggar++ input)
  6 degree of freedom solver (w/ constraints, restraints, loads)

## Slide 12: Orphan Points
LSQ nearest neighbor averaging
“Neighborhood” user selectable: radius and levels
Remediation fully parallel
Same approach used for changing iblank (dynamic)
oversetFvMeshCoeffs
{
DiRTlibNumberOfVariables 3;
dciFilePrefix "output";
searchRadiusFactor 3.4;
maxCellCellRows 4;
nOrphanIterations 50;
tolOrphanIterations 0.05;
...
}

## Slide 13: libSuggar++
oversetFvMeshCoeffs
{
...
writeComponentCellSets false;
writeDynBodiesCellSets false;
useLibSuggar++ true;
// Only libSuggar++
DCIMemoryTransfer true;
nSuggarRanks 1;
motionMemoryTransfer true;
motionFileOutput true;
motionOutputDCIFile false;
}
More complex prescribed and dynamic motions need libSuggar++

## Slide 14: 6 Degrees of Freedom
Available integrators
  Symplectic
  Newmark
  Crank-Nicholson
Constraints: point, axis, line, plane, orientation
Restraints: linear spring, linear and angular damper
Loads: external force and moment
Selectable gravity, buoyancy and hydrodynamic forces

## Slide 15: Body Hierarchy
No limit on number of bodies or levels
Only limit: no 6DoF-in-6DoF
multiOversetBodyMotionFvMeshCoeffs
{
helicopter
{
oversetBodyMotionFunction linearMotion;
linearMotionCoeffs
{
}
main-rotor
{
oversetBodyMotionFunction rotatingMotion;
rotatingMotionCoeffs
{
}
blade1
{
oversetBodyMotionFunction oscillatingRotatingMotion;
oscillatingRotatingMotionCoeffs
{
}
}
}
}
}

## Slide 16: Parallel
Solver
  Usual decomposition methods available
  No restriction on how or where mesh is decomposed
Overset (libSuggar++) currently runs in parallel on solver ranks
  No MPI_COMM splitting (yet)
  No DC groups (yet)
Suggar++
Caelus
Suggar++
Caelus
Caelus
Suggar++ DC groups

## Slide 17: Solvers
Will initially provide:
  Single phase: static and dynamic
  Multi-phase (VOF): static and dynamic
Adding solvers “should” be trivial

## Slide 18: Utilities
Move component grids with:
  Prescribed motion (DCI files)
  motion.xml
Create overset data: iblank, component ids
Compute mass and moment of inertial properties of bodies

## Slide 19: Static Validation

## Slide 20: 6 DoF Validation

## Slide 21: Availability
Yes
Open-source but not free (as in beer)

## Slide 22: What is ?
Caelus is a derivative of OpenFOAM
Open and free (as in beer): www.caelus-cml.com
Supports multiple platforms (Windows, Linux and Mac)
Robust compilation: Scons
Easy to install
Verified schemes and Validated solvers and turbulence models
Documentation and validation cases
Improved algorithmic robustness on non-”perfect” meshes
Improved accuracy on non-”perfect” meshes
Swak, Python wrapping, etc
New compressible solvers and turbulence models
New VLES turbulence model class
Stable, predictable API

## Slide 23: What is Caelus?
Documentation and validation cases
Easy installation with minimal dependencies (Python and MPI)

## Slide 24: What we do
Specialise in the application, support and development of open source computational mechanics
Provides customer value by conducting industry-relevant TRL 2-6 R&D
Engage with customers as their technology partner
Industry Relevant Research

## Slide 25: Technology Summary
Solvers
  Highly efficient incompressible/compressible fractional-step solvers (AIAA Scitech 2015)
Combustion
  Arrhenius finite-rate chemistry models (GTP 2015)
  Thermo-acoustic instability solvers (JPP 2015)
Sensitivity, Optimization and Uncertainty (SOU)
  Adjoint (SAE 2014)
  Tangent
  Uncertainty and error propagation
Turbulence modelling
  VLES (APISAT 2015)
Acoustics solvers (JPP 2015)
  Linearized Euler
  Linearized Perturbed Compressible Equations (LPCE)
Overset

## Slide 26: Current Research Projects
Multi-scale multiphase solver
Employ adjoint, tangent, polynomial chaos to:
  Optimize for acoustic phenomena
  Investigate uncertainty and error propagation of turbulence parameters and quantities (e.g. empirical coefficients)
Automated vertically integrated CFD workflows:
  Meshing → Solving → Post-pro → SOU → Meshing …
Development of generic overset framework (solver agnostic) to enable:
  Higher quality meshes
  Multiple, nested dynamic body motions

## Slide 27: Semi Linear Implicit Method - SLIM
Fast, low dissipation fractional step solver based on projection method
Significantly better scalability than traditional implicit transient solvers
4X
Industrial parallel performance study of 50 million cell ABL simulation

## Slide 28: Adjoint
Time-symmetry preserving semi-discrete surface adjoint:
  Provides both direction and magnitude
Tested on meshes up to 60M cells without limitation
Used to redesign front air dam on V8 supercar

## Slide 29: VLES: Hybrid RANS/DES Turbulence Model
Based off of Speziale, C. G. (1998) “Turbulence modeling for time-dependent RANS and VLES: A review”, AIAA J., 36, pp. 173–184.
Use resolution function, Fr, off body to blend RANS and LES
Rear wheel pressure coefficient
Rudimentary Landing Gear , AIAA Aeroacoustics Workshop

## Slide 30: Who we are
Darrin Stephens
has an extensive background in modeling a range of complex reacting multiphase flows and led the development of CFD models for a number of industrial unit processes allowing re-design and optimization, improving throughput and efficiencies. He is the managing director and principle research engineer at Applied CCM Pty Ltd., a company providing development, technical support and training for the open source CFD software OpenFOAM. His professional interests include multi-phase algorithms, optimization algorithms, population balance modeling, coupled solvers and the development of next-generation hybrid and multi-physics models. He earned his Ph.D. degrees in mechanical engineering from James Cook University in Townsville, Australia.
Chris Sideroff
is the managing director and principle research engineer at Applied CCM Canada, a company providing development, technical support and training for open source based CFD software such as Caelus and OpenFOAM. His current research interests are automation methods for mesh generation, more robust discretization schemes for highly anisotropic and skewed meshes for finite volume based CFD solvers, work flow automation (pre, solve, post) with interpreted programming languages such as Python, and overset grid technologies. He earned his Ph.D. degree in mechanical and aerospace engineering from Syracuse University in Syracuse, USA.
Aleks Jemcov
has 20 years of experience in computational fluid dynamics and turbomachinery related flows. His research interests include development of numerical algorithms for fluid mechanics, solid-fluid interactions, efficient solver methodologies applicable to both compressible and incompressible flows, thermo-acoustics, turbulence modeling, and linear algebra. Prior experience includes work in the Combustion Dept. at Pratt & Whitney Canada, Development Dept. at Fluent Inc., and the Development Department and Fluids Business Unit at ANSYS, Inc. He currently serves as Associate Director for Computational Sciences at the Notre Dame Turbomachinery Laboratory and is a Research Assistant Professor in the Aerospace and Mechanical Engineering Department at the University of Notre Dame. He earned his Ph.D. in Aerospace Engineering from the University of Belgrade.

## Slide 31
Applied CCM Inc
Dr Chris Sideroff
Phone: +1 613 276 7472
Email: c.sideroff@appliedccm.ca
Web: www.appliedccm.com
Questions
Applied CCM Pty Ltd
Dr Darrin Stephens
Phone: +61 03 8376 6962
Email: d.stephens@appliedccm.com.au
Web: www.appliedccm.com
www.caelus-cml.com