## Slide 1
Rotor Hub Flow Simulations Using the OVERFLOW Solver
Presented at the 13th Overset Grid Symposium
Mukilteo, WA
October 18, 2016
Dr. Jim Coder
University of Tennessee – Knoxville
Dr. Norman F. Foster and Mr. Warren J. Baker
Penn State Applied Research Laboratory

## Slide 2: Background and Motivation
Rotor hub accounts for ~30% of the parasite drag for rotorcraft at high speeds
Complex flow physics
  Rotating, unsteady
  Transitional
  Large amounts of separation
  Interactional aerodynamics
Ongoing experimental and computational investigations at PSU, UTK, and GIT
  Supported through VLC and VLRCOE
Reich et al.

## Slide 3: Background and Motivation
1st Rotor Hub Flow Prediction Workshop held at Penn State in June 2016
  Assess the state of the art and best practices for predicting rotor hub flows
  Simulate an experiment conducted in the 48” Garfield Thomas Water Tunnel at Penn State ARL
  Focus on the wake near and long-age wake predictions
  Representatives from academia, government and industry
Structured, overset methods are well suited for hub flows
  Complex geometries
  Structured grids amenable to high-order differencing schemes

## Slide 4: Objectives and Strategy
Using OVERFLOW 2.2i with a fully turbulent, hybrid RANS/LES method and higher-order convective fluxes
  Structured, overset solver
  Density-based, compressible, ideal gas
Hybrid RANS/LES methods prevent excessive turbulent dissipation in wakes
Higher-order fluxes beneficial for vortex-dominated flow fields and helps preserve key flow structures
Test cases considered for simulations
  μ = 0.20, Re = 4.6 x 106 – current focus
  μ = 0.20, Re = 2.3 x 106

## Slide 5: Approach

## Slide 6: Preliminary Grid System
Simplified geometry
  99 total grids, 17 million cells
  Not sublayer resolved (y+ >> 1)
  Includes pylon and test-section walls
Used to verify solution strategies

## Slide 7: Revised Grid System

## Slide 8: Revised Grid System
Structured, overset mesh generated by ARL-PSU
138 total grids
  10 stationary
  128 rotating
  Includes pylon and test-section walls
48.3 million total grid points
Sublayer resolved mesh
  Δy ≈ 0.0001”
  Except tunnel walls

## Slide 9: Turbulence Modeling
Spalart-Allmaras model with DDES
  One-equation turbulence model
  DDES provides hybrid RANS/LES-like behavior in separated regions and wakes
    d is the distance to the nearest solid wall
    fd is a blending function to switch between RANS and LES branches
    Δ is the local grid spacing
    CDES is detached-eddy-simulation calibration coefficient

## Slide 10: Numerical Methodology
‘Free-stream’ inlet/outlet conditions
  M∞ = 0.1
  Re = 191667 in-1 (Re = 4.6 x 106) and 95833 in-1 (Re = 2.3 x 106)
  μt/μ = 0.1
  Characteristic BC used for both inlet and outlet
Viscous, no-slip walls used for all solid surfaces
  Pressure extrapolation
Hub motion prescribed using Config and Scenario XML files
  μ = 0.2 based on full rotor radius (Rhub = 0.15Rrotor)
    ω = 0.0625 rad/s*

## Slide 11: Numerical Methodology
XRAY hole cutting and OVERFLOW internal DCFCRT routines
  XRAYs defined using Chimera Grid Tools
  Three fringe layers to accommodate 5th-order upwind scheme
  Viscous stencil repair used within 18 points of the wall
  Result: 30 orphans

## Slide 12: Numerical Methodology
Time-accurate solution settings
  Implicit BDF2 integration
  5th-order-accurate WENO right-hand side
    WENO5M limiter
    No artificial dissipation
    No low-Mach preconditioning
  D3ADI left-hand side
    SSOR solver too slow, and difficulty stabilizing ARC3D scalar-pentadiagonal scheme for specified RHS
  SA-RC-DDES
  Δt set to give 0.25° per step
  Newton subiteration used to converge unsteady residual 3 orders of magnitude
    Maximum of 50 specified, 16-28 generally required

## Slide 13: Numerical Methodology
Solutions initialized with 5000 non-time-accurate iterations
  Goal is to get bulk, large-scale flow features set up
  DDES active to prevent excessive turbulence
  3rd-order Roe RHS, ARC3D scalar-pentadiagonal LHS
    2nd/4th non-linear artificial dissipation with 10.0 and 0.1, respectively
    Low-Mach preconditioning
Switch to time-accurate
  Four complete rotations (5760 iterations) without data sampling
    Approx. 2.5 test-section lengths simulated
  Four more complete rotations with data sampling
    Solutions saved every 2° (8 iterations)

## Slide 14: HPC Performance
XRAYs and DCF hole cutting debugged on local machine
  35 minutes per manual iteration
AFRL HPC Lightning (Cray XC30) used for calculations
  8 nodes, 24 cores per node (192 cores total)
  42.3 seconds (average) per iteration
    Flow solver: 34.00 seconds/iteration (average)
    DCF: 1.21 seconds/iteration
    File I/O: 12.03 seconds per save
  Solver diagnostics estimated a 185.5x speedup (97% efficiency)

## Slide 15: Results

## Slide 16: Streamwise Velocity Profiles, Re = 4.6 x 106
Chart: u/U∞
| 0.85661153846153826 | 0.67793261538461524 | 0.61418123076923103 | 0.56690153846153923 | 0.54361753846153904 | 0.56678138461538519 | 0.5799044615384622
X/R = 2.09, Z/R = -0.19 | -0.66 | -0.43767 | -0.21533 | -0.10417 | 0.007 | 0.22933 | 0.45167
X/R = 4.14, Z/R = -0.19 | -0.66 | -0.43767 | -0.21533 | -0.10417 | 0.007 | 0.22933 | 0.45167
X/R = 7.15, Z/R = -0.19 | -0.66 | -0.43767 | -0.21533 | -0.10417 | 0.007 | 0.22933 | 0.45167

## Slide 17: Streamwise Velocity Profiles, Re = 4.6 x 106
Chart: u/U∞
| 0.48350230769230812 | 0.44971584615384602 | 0.56690153846153923 | 0.83176538461538518 | 0.94548107692307726
X/R = 2.09, Y/R = -0.10 | -0.41833 | -0.31417 | -0.18917 | -0.0225 | 0.14417
X/R = 4.14, Y/R = -0.10 | -0.41833 | -0.31417 | -0.18917 | -0.0225 | 0.14417
X/R = 7.15, Y/R = -0.10 | -0.41833 | -0.31417 | -0.18917 | -0.0225 | 0.14417

## Slide 18: Wake Velocities, Re = 4.6 x 106

## Slide 19: Near-Wake, Re = 4.6 x 106

## Slide 20: Mid-Wake, Re = 4.6 x 106

## Slide 21: Far-Wake, Re = 4.6 x 106

## Slide 22: Wake Behavior, Re = 4.6 x 106

## Slide 23: Wake Behavior, Re = 4.6 x 106

## Slide 24: Outlet-Induced Pressure Behaviors
Undesirable behavior of outlet boundary condition
  Expected cleaner outflow behavior
  Wave accumulation affecting upstream behavior
4R
7R
2R

## Slide 25: Intermediate Observations
Wake refinement region too coarse
  Large jump in cell size from body-fitted grids
  Unintended cell anisotropy – 0.5” x 0.5” x 1”
Blockage effects not well modeled
  Density-based solver requires total conditions on inlet boundary
  More appropriate to specify a mass-flow rate, but unsteady effects make this difficult
Outlet boundary exhibiting unexpected pressure behavior
  Likely due to characteristic boundary condition and/or higher-order differencing in convective fluxes
  May be contaminating upstream wake development
  Sponge layer may improve solution quality

## Slide 26: Improved Simulations (Ongoing)

## Slide 27: New Off-Body Grid System
Grid Enhancements
  Enlarged wake-refinement region
  Isotropic, 0.25-inch cells in wake-refinement region
  Slight refinement of tunnel background mesh
    Reduced y+ value, still not sublayer resolved
  Addition of upstream and downstream coarse “sponge” layers
  New size: 57.5M nodes
Modified BCs
  Characteristics-based nozzle inflow
  Constant pressure outflow, P/P∞ = 1
  Inviscid walls upstream of test section
  Viscous walls downstream of test section

## Slide 28: New Off-Body Grid System

## Slide 29: Sample Wake Behavior
Identical numerical method as previous simulation
  Implicit BDF2, 0.25° timestep, 5th-order WENO RHS, D3ADI LHS, SA-RC-DDES, Newton subiterations with 3-order convergence

## Slide 30: Conclusions and Future Work

## Slide 31: Conclusions
Enhanced grid system greatly improved solution quality
  Better matching of body-fitted and background grids
  Turbulent wake content better resolved and preserved downstream
Changing the inlet/outlet boundary conditions helped
  Still not perfect, approx. 5% error in effective Reynolds number
  Specified mass-flow condition preferred, but difficult to enforce in unsteady flow
Mid- and long-age wake characteristics appear to show sensitivity to axial pressure gradient
  Under continuing investigation

## Slide 32: Future Work
Explore the impact of physical modeling
  Laminar-turbulent transition
  QCR
  Scale-adaptive simulation
Assess the influence of the tunnel wall boundary layer on the wake behavior
  Water tunnel has constant-diameter test section with non-negligible buoyancy correction
  Could be the difference between a favorable and an adverse axial pressure gradient

## Slide 33: Acknowledgments
The authors are grateful to the US Army’s National Rotorcraft Technology Center program and Dr. Louis Centolanza for funding this research. Effort This effort was sponsored by the US Government under Other Transaction number W15QKN-10-9-0003 between Vertical Lift Consortium, Inc. and the Government, project NRTC-FY15-R-01. The US Government is authorized to reproduce and distribute reprints for Governmental purposes notwithstanding any copyright notation thereon. The views and conclusions contained herein are those of the authors and should not be interpreted as necessarily representing the official policies or endorsements, either expressed or implied, of the US Government.

## Slide 34: Questions?