## Slide 1
Approved for public release; distribution unlimited.
Review completed by the AMRDEC Public Affairs Office (PR2263, 23 May 2016)
DISCLAIMER: Reference herein to any specific commercial, private or public products, process, or service by trade name, trademark, manufacturer, or otherwise, does not constitute or imply its endorsement, recommendation, or favoring by the United States Government. The viewing of the presentation by the Government shall not be used as a basis of advertising.
Application of Strand Grid Framework to Rotorcraft Simulations
13th Symposium on Overset Composite Grids and Solution Technology
Mukilteo, WA
October 18, 2016
Vinod Lakshminarayan
Science & Technology Corporation
NASA Ames Research Center
Moffett Field, CA
Jayanarayanan Sitaraman, Parallel Geometric Alg. LLC
Andrew Wissink, US Army Aviation Development Directorate

## Slide 2: Strand Grid Framework
“Strands” grown directly from Surface Tessellation
Introduced by Meakin et al, 2007
“Strand” near-body grid
  Straight line segments grown directly from surface tessellation
  Extrudes a short distance
  Transitions from viscous spacing at a specified wake spacing
  Can self-intersect
Cartesian AMR off-body grid
  Covers rest of the domain

## Slide 3: Strand Grid Framework
Advantages
“Nearly automatic” mesh generation
  Only three inputs : surface tessellation, viscous spacing, wake spacing
  Haimes, 2014 – 2016  MOSS code
Strands represented with minimal information
  Mesh can be stored in all processors
  Highly parallel domain connectivity
  Sitaraman et al. 2012  OSCAR
Facilitate efficient flow solvers
  Line-based solution methodology
  Lakshminarayan et al. 2016  mStrand
This work
Shows validation of strand grid framework using mStrand for rotorcraft problems
Surface Tessellation
Viscous spacing
Off-body mesh automatically refined to wake spacing

## Slide 4
Multi-strand Solver (mStrand)
Solver Features
2nd order vertex centered FV solver
Surface grid can be quads or/and triangles
General prismatic mesh in normal direction
Robust treatment of multiple strand per surface node
MUSCL reconstruction + Riemann solver along strands as well as in the “r-s” plane  Spurious oscillation prevented using gradient-based limiters
2nd order full Navier-Stokes term  Gradients computed using Weighted Least-Squares or Green-Gauss method
1st order implementation of SA turbulence model
Linear solver using preconditioned GMRES
Fully parallel
Developed from Nov 2014 -

## Slide 5: Helios Framework
Supports high-fidelity rotary-wing simulation by government and industry
Developed & maintained by a team at Army ADD.
Dual Mesh Paradigm
Near-body
Cartesian off-body
CFD/CSD Coupling
Adaptive Mesh Refinement
To resolve wake
RCAS and CAMRAD Structural Dynamics and Trim coupling
Advanced Software Infrastructure
Python-based infrastructure readily supports addition of new software
HPCMP CREATETM AV Helios Helicopter Overset Simulations
High Performance Computing
Runs on HPC hardware with focus on parallel scalability
Rotor-Fuselage and Multi-rotor moving mesh support
Moving Body Overset
mStrand
near-body solver
SAMCART
off-body solver

## Slide 6
Test Cases
Tram rotor in hover
UH-60A high altitude stalled flight (C9017)
HART II Blade-Vortex Interaction problem

## Slide 7
Mesh Generation
MOSS Code by Haimes
Intended to be used directly to generate all meshes
Able to generate meshes for all geometry considered
Generated volume mesh not optimal for CFD calculation
Issue with allowing only straight-line strands
Solution
Relax definition of strands  Strand represented by one or more line-segments
No. of line-segments for each strand could be different
Single line at most locations
Multiple line segments are regions with sharp corners
Compact representation of strand grid still valid
<10% overhead for most problems
Provides better control of grid quality
Strands sub-divided using specified distribution
Strand sub-divided
Problem exacerbated with fine spacing near corners

## Slide 8
Mesh Generation
Meshes in Current Work
All strands represented with same no. of line-segments
Multi-level strategy
MOSS for the first level  Multi-stranded mesh
Outer boundary of a level used as starting point for next
Levels grown using simple normal smoothing strategy
<10 levels required for good CFD meshes
Working on robust algorithm to grow levels
Single-level mesh from MOSS
First level using MOSS
Next-level starts at outer-boundary of first-level
Mesh using 9 levels

## Slide 9
Tram Rotor in Hover
Aspect ratio  10.36
Tip Mach  0.62
Tip Re number  2.1 million
Collective  6o - 16o
Grid
Single stranded mesh
Quad + Tri surface mesh
Each body meshed separately
~6.7 million NB (51 strand layers)
Calculations run for 8 revs – 11,520 steps with a rotor step of 0.25o.
Off-body mesh adapted every 10 steps
2 days on 1024 procs
Quarter-scale V22
Test developed by NASA and U.S. Army
Interface between blade, hub and Cartesian mesh

## Slide 10
Tram Rotor in Hover
Power vs Thrust
Figure of Merit vs Thrust
Helios/NSU3D provides benchmark best available results from Helios
Excellent performance prediction

## Slide 11
Tram Rotor in Hover
Θ = 6o
Θ = 10o
Θ = 14o
Iso-surface of q-criterion with vorticity magnitude
Tip vortices very well resolved  Vortex formation captured well
Twisting of vortices evident
Vortex interactions

## Slide 12: UH60 High-Altitude Stall Flight, C9017 - m = 0.24
Simulation Setup
Time step 0.25 deg azimuth
8 sub-iterations/time step in near-body
20 sub-iterations/time step in off-body
Spalart-Allmaras turbulence model with rotation correction
Strand Grid
Blade-only simulation
1.6M points per blade (61 layers)
Multi-stranded at trailing edge
Strand grid
Extends 0.5 chords
NASA/U.S. Army UH-60A Airloads Program
4-bladed rotor – 322in radius
Chord at unswept portion – 20.76in
Rotor speed – 258RPM

## Slide 13: UH60 High-Altitude Stall Flight, C9017 - m = 0.24
Satisfactory solver convergence
Solver Convergence
Airload Convergence
Fully coupled CFD/CSD simulation  RCAS for structural dynamics and trim
Loose coupling strategy  Forces and deformations over a period
4 rotor revolutions for convergence  5760 steps and 15 coupling iterations
AMR off-body Cartesian grid  57M nodes
Less than 2 days on 720 procs

## Slide 14: Airloads Comparison (C9017) – Normal Force
r/R = 0.4
r/R = 0.67
r/R = 0.96
r/R = 0.86

## Slide 15: Airloads Comparison (C9017) – Pitching Moment
r/R = 0.4
r/R = 0.67
r/R = 0.96
r/R = 0.86
Overall good agreement

## Slide 16: Predicted Wake – C9017
Wake well captured
Off-body grid has refined based on solution
Unsteadiness in the wake
Iso-surface of q-criterion

## Slide 17: HART II Blade-Vortex Interaction
4-bladed rotor
2m radius and 0.121m chord
Tests conducted at DNW wind tunnel
Descending flight at μ = 0.15
Strand Grid
3.5million per blade
0.67million
Multi-stranded at tip
Extends 0.3 chords

## Slide 18: Other CFD Data
Other CFD Data for Comparison  Jayaraman et al. 2016
Blade grid extends to one chord from surface
FUN3D blade grid
  3.5M nodes mixed element grid – Comparable number of nodes in strand mesh
  Refinement in the tip region – Similar surface grid as strand mesh
OVERFLOW blade grid
  5M nodes per blade
  Fine mesh with 2% chord spacing from 80% to tip
Identical off-body grid
500M off-body grid points
FUN3D and OVERFLOW in Helios,

## Slide 19: Simulation Parameters
Near-body solver  2 orders
Off-body solver  3.5 orders
Solver Convergence
Prescribed blade motions from a previously coupled simulation
Time step 0.1 deg azimuth (3600 time steps/rev)
4 full rotor revolutions for convergence – 14400 steps
8 sub-iterations per time step for near-body
12 sub-iterations per time step for off-body
DES in the off-body
4 days on 3600 procs on HPC

## Slide 20: Airloads Comparison
Strand grid framework results agree well with other CFD
All CFD comparable to experiment
BVI events well captured
At 87% spanwise station

## Slide 21: Experimental PIV Location
Y = 70o
Y = 20o
y/R = 0.7
y/R = 0.7
Vortex Roll-up
Measurement 17a, Y = 51o, vortex wake age = 5.3o
Measurement 17b-d, 17, 17e-h, dY = 5o, wake age  10.3o to 45.3o
Vortex Convection
Measurement 17-19, Y = 70o, wake age  25.3o to 205.3o
Measurement 20-23, Y = 20o , wake age  245.3o to 515.3o

## Slide 22: Prediction of Vortex Roll-up
y/R = 0.7
Measurement 17a, Y = 51o
Measurement 17b-d, 17, 17e-h, dY = 5o
Vortex strength comparable to FUN3D
Wake age of 5.3o – 45.3o

## Slide 23: Prediction of Vortex Roll-up
Vortex formation and evolution well-captured within strand grid
Solution dissipated when transferred to off-body
Vortex transferred to off-body at younger wake age
Need to exercise AMR in off-body with additional levels
OVERFLOW as near-body solver in Helios
Strand grid framework in Helios

## Slide 24: Prediction of Vortex Convection
Y = 70o
Y = 20o
y/R = 0.7
y/R = 0.7
Vortices well identified
Measurement 17-19, Y = 70o
Measurement 20-23, Y = 20o

## Slide 25: Wake Comparison – Positions 17-23
Vortex position predicted similar to other CFD
Vortex strength at position 17
  Comparable to FUN3D
  Lower than OVERFLOW
Vortex strength at position 18-23
  Comparable or better than OVERFLOW
Vortex Position
Vortex Strength
Y = 70o
Y = 20o
y/R = 0.7

## Slide 26: Predicted Wake
Tip
Iso-surface of Q-criterion
Several interaction of vortices with blade
Returning vortex has less chance of re-entering coarser portion of blade grid
Coarser inboard portion
Tip Vortex
Returning Vortices

## Slide 27
Code Performance
Performance for TRAM blade simulation compared with established structured and unstructured solvers
OVERFLOW – NASA structured grid solver
NSU3D – Univ. of Wyoming unstructured grid solver
mStrand grid
NSU3D grid
OVERFLOW grid
TRAM case without hub
~6.4 million grid points

## Slide 28
Code Performance
OVERFLOW – Structured grid solver
NSU3D – Unstructured grid solver
Two orders sub-iteration convergence sought
Set max number of sub-iterations
Codes tested on different number of procs
mStrand  best turn-around time at NCPU = 1440

## Slide 29
Concluding Remarks
Demonstrated ability to accurately simulate rotorcraft problems with complex physics using strand-grid framework
  mStrand able to handle deforming blades, CFD/CSD coupling
  Airloads and stall well predicted
  Able to predict wake comparable to established solution procedure
Strand technology is promising with the ability to automate solution procedure; at the same time provide good solver efficiency
Future Work
Address meshing challenges for complex geometries
Simulate helicopters with complex fuselage

## Slide 30
Acknowledgments
Material presented in this paper is a product of the CREATETM-AV Element of the Computational Research and Engineering for Acquisition Tools and Environment (CREATETM) Program sponsored by the U.S. Department of Defense HPC Modernization Program Office. We also the support of U.S. Army for this work. The authors would like acknowledge Mark Potsdam, Buvana Jayaraman and Beatrice Roget for providing help in setting up various cases.